## Slide 1: Defensive Charging: Mitigating Power Side-Channel Attacks on Charging Smartphones
Shyam Kumar Reddy
Master of Science in Data Science
Email id:sannapur001@gannon.edu

## Slide 2: Table of Content:
INTRODUCTION
RELATED WORK
ATTACK DETAILS AND IMPLEMENTATION
PROPOSED DEFENSE MECHANISMS
EXPERIMENTAL DESIGN AND SETUP
ATTACK AND DEFENSE EVALUATIONS
EFFICIENCY OF THE DEFENSE MECHANISMS
DISCUSSION AND CONCLUSIONS

## Slide 3: INTRODUCTION
Mobile is the essential part of life in today world.
Studies says users charges their mobile 3 times a day from different places with include the public places too that increases the chances of the attacker to interfere the user activity.
Two schemes to mitigate this family of attacks.
  hardware-based solution
    Design and evaluation of power side-channel attacks on phone charging
    Hardware-based defense against power side-channel attacks on the smartphone charging process
  software-based solution
    Software-based defense against power side-channel attacks on the smartphone charging process

## Slide 4: RELATED WORK
In the cryptography domain to mitigate these attacks we have some philosophy.
  Leakage reduction
  Noise introduction
  Incorporation of randomness (e.g., addition of randomness in the data input to the cipher system while still ensuring correctness of the results).
  All that the attacker would have to do is replace a victim’s phone battery with a malicious smart battery, collect power traces from the malicious smart battery, and use machine learning algorithms to make inferences on the victim’s activities while using the phone.
  Two significant differences between our work and the work by Lifshits
    Defense Vs Attack Objectives : focused on the design, implementation and evaluation of two defense mechanisms against power side-channels on the phone charging process.
    Differences in the Attacks Studied: an implementation and evaluation of three different attacks on the charging process.

## Slide 5: ATTACK DETAILS AND IMPLEMENTATION
we first describe a threat model that expresses the capabilities and targets of the attacker.
Models to control the attacks
  Threat Model : Threat model assumes a victim undertaking activities on a smartphone which is plugged into a charging station.
    Two primary forms of information that the attacker will be interested in include:
      The identities of keys typed by the victim
      Activities the user performs on the phone
  Implementation of the Attacks
    Data Acquisition
    Feature Extraction
    Classification

## Slide 6: PROPOSED DEFENSE MECHANISMS
Hardware-Based Defense
  Scrambler System Hardware.
  Scrambler System Firmware.
Software-Based Defense
  Design and Implementation Requirements
  Choice of Defense Operations
  Defense Design and Implementation.

## Slide 7: EXPERIMENTAL DESIGN AND SETUP
Data Collection Experiments: Collect data that we used to illustrate the attack (i.e., power signals were captured without perturbations by the defense), while the other two were used to collect data that we used to illustrate the two defense mechanisms
  Attack Experiment : Consisted of connecting the smartphone(s) to our power meter via USB and collecting power traces tailored to the specific activity (web browsing, key tapping, or phone call) while the phone was charging.
  Hardware-Based Defense Experiment : we used the hardware defense solution (scrambler), Instead of connecting the phone directly to the power meter, the phone was connected to the power meter via the defense scrambler.
  Software-Based Defense Experiment: we used the software defense solution .The setup of this experiment is similar to that in Experiment (1) above, except that the phone in this case had the software defense solution running during data collection.
Data Collection Tools
  Power Trace Collecting Equipment: To emulate the malicious USB power charging station, we built a simple power meter using an MSP430 micro-controller similar to the one used in the hardware scrambler circuit
  Smartphones and Software Used: We used the Samsung Galaxy S5 and Samsung Galaxy S6, both running Android OS, Version 6.0.1 (Marshmallow) to collect power traces in all our experiments.

## Slide 8: ATTACK AND DEFENSE EVALUATIONS
we describe the data collection procedure used and then present the performance of the attack without the use of any defense mechanism.
  Attack vs Defense Scenario
  Defense vs Defense Scenario
Website Inference Attack
Keystroke Inference Attack
Incoming Call Detection Attack

## Slide 9: EFFICIENCY OF THE DEFENSE MECHANISMS
Impact on Charging Times
Impact on CPU and Memory Utilization
Adoption Impact Analysis for Energy Consumption and CO2 Emissions

## Slide 10: DISCUSSION AND CONCLUSIONS
we demonstrated two highly effective measures against power analytics attacks on smartphone charging systems.
Our results in Section 7 show a minimal impact on the user through increased charging times (less than 10% increase) or additional resource consumption (CPU and Memory) on their phone.
These results confirm that the principle of our defenses work under a reasonable set of assumptions.